ORDINANCE NO. 2011-03

AN ORDINANCE AMENDING SECTION 802.03 OF THE CITY CODE AS IT RELATES TO FLOOD PLAIN MANAGEMENT

The City Council of the City of Mendota hereby ordains:

Section 1.  That Section 802.03 of the City Code is hereby deleted and amended with the following floodplain ordinance:

Section 802.03

Floodplain Management

# SECTION  802.03   STATUTORY AUTHORIZATION, FINDINGS OF FACT AND PURPOSE

802.031 Statutory Authorization:  The legislature of the State of Minnesota has, in Minnesota Statutes Chapter 103F and Chapter 462 delegated the responsibility to local government units to adopt regulations designed to minimize flood losses.  Therefore, the Mendota City Council of the City of Mendota, Minnesota does ordain as follows:

802.032 Findings of Fact:

802.0321  	 The flood hazard areas of the City of Mendota, Minnesota, are subject to periodic 	inundation which results in potential loss of life, loss of property, health and safety hazards, 	disruption of commerce and governmental services, extraordinary public expenditures or 	flood protection and relief, and impairment of the tax base, all of which adversely affect the 	public health, safety, and general welfare.

802.0322   	Methods Used to Analyze Flood Hazards.  This Ordinance is based upon a reasonable 	method of analyzing flood hazards which is consistent with the standards established by the 	Minnesota Department of Natural Resources.

802.0323	National Flood Insurance Program Compliance.  This Ordinance is adopted to comply with 		the rules and regulations of the National Flood Insurance Program codified as 44 Code of 		Federal Regulations Parts 59 -78, as amended, so as to maintain the community’s eligibility 		in the National Flood Insurance Program.

802.033 Statement of Purpose:  It is the purpose of this Ordinance to promote the public health, safety, and general welfare and to minimize those losses described in Section 802.0321 by provisions contained herein.

# SECTION  802.04 GENERAL PROVISIONS

802.041 Lands to Which Ordinance Applies:  This Ordinance shall apply to all lands within the jurisdiction of   the City of Mendota shown on the Official Zoning Map and/or the attachments thereto as being located within the boundaries of the Floodway and Flood Fringe Districts.

802.042 Establishment of Official Zoning Map:  The Official Zoning Map together with all materials attached thereto is hereby adopted by reference and declared to be a part of this Ordinance.  The attached material shall include the Flood Insurance Study for the Dakota County, Minnesota And Incorporated Areas and Flood Insurance Rate Map panels therein numbered 27037C0018E and 27037C0019E, all dated December 2, 2011 and prepared by the Federal Emergency Management Agency. The Official Zoning Map shall be on file in the Office of the City Clerk.

802.043 Regulatory Flood Protection Elevation:  The regulatory flood protection elevation shall be an elevation no lower than one foot above the elevation of the regional flood plus any increases in flood elevation caused by encroachments on the flood plain that result from designation of a floodway.

802.044 Interpretation:

802.0441  In their interpretation and application, the provisions of this Ordinance shall be held to be                                         	         minimum requirements and shall be liberally construed in favor of the Governing Body and 		         shall not be deemed a limitation or repeal of any other powers granted by state statutes.

  - Boundaries of the zoning districts shall be determined by scaling distances on the Official Zoning Map.  Where interpretation is needed as to the exact location of the boundaries of the district as shown on the Official Zoning Map, as for example where there appears to be a conflict between a mapped boundary and actual field conditions and there is a formal appeal of the decision of the Zoning Administrator, the Board of Adjustment shall make the necessary interpretation.  All decisions will be based on elevations on the regional (100-year) flood profile, the ground elevations that existed on the site at the time the Community adopted its initial floodplain ordinance or on the date of the first National Flood Insurance Program map showing the area within the 100-year floodplain if earlier, and other available technical data.  Persons contesting the location of the district boundaries shall be given a reasonable opportunity to present their case to the Board of Adjustment and to submit technical evidence.

802.045 Abrogation and Greater Restrictions:  It is not intended by this Ordinance to repeal, abrogate, or impair any existing easements, covenants, or deed restrictions.  However, where this Ordinance imposes greater restrictions, the provisions of this Ordinance shall prevail.  All other ordinances inconsistent with this Ordinance are hereby repealed to the extent of the inconsistency only.

802.046 Warning and Disclaimer of Liability:  This Ordinance does not imply that areas outside the flood plain districts or land uses permitted within such districts will be free from flooding or flood damages.  This Ordinance shall not create liability on the part of the City of Mendota or any officer or employee thereof for any flood damages that result from reliance on this Ordinance or any administrative decision lawfully made thereunder.

802.047 Severability:  If any section, clause, provision, or portion of this Ordinance is adjudged unconstitutional or invalid by a court of competent jurisdiction, the remainder of this Ordinance shall not be affected thereby.

802.048 Definitions:  Unless specifically defined below, words or phrases used in this Ordinance shall be 	interpreted so as to give them the same meaning as they have in common usage and so as to give this 	Ordinance its most reasonable application.

802.0481 	Accessory Use or Structure - a use or structure on the same lot with, and of a nature          	customarily incidental and subordinate to, the principal use or structure.

802.0482 	Basement - means any area of a structure, including crawl spaces, having its floor or base 	subgrade (below ground level) on all four sides, regardless of the depth of excavation below 	ground level.

802.0483	 Conditional Use - means a specific type of structure or land use listed in the official control 	that may be allowed but only after an in-depth review procedure and with appropriate 	conditions or restrictions as provided in the official zoning controls or building codes and 	upon a finding that:

(a)Certain conditions as detailed in the zoning ordinance exist.

(b)The structure and/or land use conform to the comprehensive land use plan if one exists 	     and are compatible with the existing neighborhood.

802.0484 	Equal Degree of Encroachment - a method of determining the location of floodway 	boundaries so that flood plain lands on both sides of a stream are capable of conveying a 	proportionate share of flood flows.

802.0485 	Flood - a temporary increase in the flow or stage of a stream or in the stage of a wetland or 	lake that results in the inundation of normally dry areas.

802.0486 	Flood Frequency - the frequency for which it is expected that a specific flood stage or 	discharge may be equaled or exceeded.

802.0487 	Flood Fringe - that portion of the flood plain outside of the floodway.  Flood fringe is 	synonymous with the term "floodway fringe" used in the Flood Insurance Study for the 	Dakota County, Minnesota And Incorporated Areas.

802.0488 	Flood Plain - the beds proper and the areas adjoining a wetland, lake or watercourse which 	have been or hereafter may be covered by the regional flood.

802.0489 	Flood Proofing - a combination of structural provisions, changes, or adjustments to 	properties and structures subject to flooding, primarily for the reduction or elimination of 	flood damages.

802.04810	 Floodway - the bed of a wetland or lake and the channel of a watercourse and those portions 	of the adjoining flood plain which are reasonably required to carry or store the regional flood 	discharge.

802.04811 	Lowest Floor - the lowest floor of the lowest enclosed area (including basement).  An 	unfinished or flood resistant enclosure, used solely for parking of vehicles, building access, 	or storage in an area other than a basement area, is not considered a building’s lowest floor.

802.04812	Manufactured Home - a structure, transportable in one or more sections, which is built on a 	permanent chassis and is designed for use with or without a permanent foundation when 	attached to the required utilities.  The term “manufactured home” does not include the term 	“recreational vehicle.”

802.04813 	Obstruction - any dam, wall, wharf, embankment, levee, dike, pile, abutment, projection, 	excavation, channel modification, culvert, building, wire, fence, stockpile, refuse, fill, 	structure, or matter in, along, across, or projecting into any channel, watercourse, or 	regulatory flood plain which may impede, retard, or change the direction of the flow of 	water, either in itself or by catching or collecting debris carried by such water.

802.04814	Principal Use or Structure - means all uses or structures that are not accessory uses or 	 	structures.

802.04815	Reach - a hydraulic engineering term to describe a longitudinal segment of a stream or river 	influenced by a natural or man-made obstruction.  In an urban area, the segment of a stream 	or river between two consecutive bridge crossings would most typically constitute a reach.

802.04816 	Recreational Vehicle - a vehicle that is built on a single chassis, is 400 square feet or less 	when measured at the largest horizontal projection, is designed to be self-propelled or 	permanently towable by a light duty truck, and is designed primarily not for use as a 	permanent dwelling but as temporary living quarters for recreational, camping, travel, or 	seasonal use.  For the purposes of this Ordinance, the term recreational vehicle shall be 	synonymous with the term travel trailer/travel vehicle.

802.04817 	Regional Flood - a flood which is representative of large floods known to have occurred 	generally in Minnesota and reasonably characteristic of what can be expected to occur on an 	average frequency in the magnitude of the 100-year recurrence interval.  Regional flood is 	synonymous with the term "base flood" used in a flood insurance study.

802.04818 	Regulatory Flood Protection Elevation - The regulatory flood protection elevation shall be 	an elevation no lower than one foot above the elevation of the regional flood plus any 	increases in flood elevation caused by encroachments on the flood plain that result from 	designation of a floodway.

802.04819 	Structure - anything constructed or erected on the ground or attached to the ground or on-site 	utilities, including, but not limited to, buildings, factories, sheds, detached garages, cabins, 	manufactured homes, recreational vehicles not meeting the exemption criteria specified in 	Section 802.1131 of this Ordinance and other similar items.

802.04820 	Substantial Damage - means damage of any origin sustained by a structure where the cost of 	restoring the structure to its before damaged condition would equal or exceed 50 percent of 	the market value of the structure before the damage occurred.

802.04821 	Substantial Improvement - within any consecutive 365-day period, any reconstruction, 	rehabilitation (including normal maintenance and repair), repair after damage, addition, or 	other improvement of a structure, the cost of which equals or exceeds 50 percent of the 	market value of the structure before the “start of construction” of the improvement.  This 	term includes structures that have incurred “substantial damage,” regardless of the actual 	repair work performed.  The term does not, however, include either:

- Any project for improvement of a structure to correct existing violations of state or local 	health, sanitary, or safety code specifications which have been identified by the local code 	enforcement official and which are the minimum necessary to assure safe living conditions.

- Any alteration of an “historic structure,” provided that the alteration will not preclude the 	structure’s continued designation as an “historic structure.”  For the purpose of this 	Ordinance, “historic structure” shall be as defined in 44 Code of Federal Regulations, Part 	59.1.

802.04822 Variance - means a modification of a specific permitted development standard required in an 	official control including this Ordinance to allow an alternative development standard not 	stated as acceptable in the official control, but only as applied to a particular property for the 	purpose of alleviating a hardship, practical difficulty or unique circumstance as defined and 	elaborated upon in a community's respective planning and zoning enabling legislation.

802.049 Annexations:  The Flood Insurance Rate Map panels adopted by reference into Section 802.042 above may include floodplain areas that lie outside of the corporate boundaries of the City of Mendota at the time of adoption of this ordinance.  If any of these floodplain land areas are annexed into the City of Mendota after the date of adoption of this ordinance, the newly annexed floodplain lands shall be subject to the provisions of this ordinance immediately upon the date of annexation into the City of Mendota.

# SECTION  802.05 ESTABLISHMENT OF ZONING DISTRICTS

802.051 Districts:

802.0511   	Floodway District.  The Floodway District shall include those areas designated as floodway                 	on the Flood Insurance Rate Map adopted in Section 802.042.

802.0512   	Flood Fringe District.  The Flood Fringe District shall include those areas designated as 	floodway fringe.  The Flood Fringe District shall include those areas shown on the Flood 	Insurance Rate Map as adopted in Section 802.042 as being within Zones AE but being 	located 	outside of the floodway.

802.052 Compliance:  No new structure or land shall hereafter be used and no structure shall be constructed, located, extended, converted, or structurally altered without full compliance with the terms of this Ordinance and other applicable regulations which apply to uses within the jurisdiction of this Ordinance.  Within the Floodway and Flood Fringe Districts, all uses not listed as permitted uses or conditional uses in Sections 802.06 and 802.07 that follow, respectively, shall be prohibited.  In addition, a caution is provided here that:

802.0521   	New manufactured homes, replacement manufactured homes and certain travel trailers and 	travel vehicles are subject to the general provisions of this Ordinance and specifically 	Section 802.11.

802.0522   	Modifications, additions, structural alterations, normal maintenance and repair, or repair 	after damage to existing nonconforming structures and nonconforming uses of structures or 	land are regulated by the general provisions of this Ordinance and specifically Section 	802.13.

802.0523  	 As-built elevations for elevated or flood proofed structures must be certified by ground 	surveys and flood proofing techniques must be designed and certified by a registered 	professional engineer or architect as specified in the general provisions of this Ordinance and 	specifically as stated in Section 802.12 of this Ordinance.

SECTION  802.06 FLOODWAY DISTRICT (FW)

802.061 Permitted Uses:

802.0611  	General farming, pasture, grazing, outdoor plant nurseries, horticulture, truck farming, 	forestry, sod farming, and wild crop harvesting.

802.0612 	Industrial-commercial loading areas, parking areas, and airport landing strips.

802.0613  	Private and public golf courses, tennis courts, driving ranges, archery ranges, picnic grounds, 	boat launching ramps, swimming areas, parks, wildlife and nature preserves, game farms, 	fish hatcheries, shooting preserves, target ranges, trap and skeet ranges, hunting and fishing 	areas, and single or multiple purpose recreational trails.

802.0614  	Residential lawns, gardens, parking areas, and play areas.

802.062 Standards for Floodway Permitted Uses:

802.0621  	The use shall have a low flood damage potential.

802.0622  	The use shall be permissible in the underlying zoning district if one exists.

802.0623  	The use shall not obstruct flood flows or increase flood elevations and shall not involve 	structures, fill, obstructions, excavations or storage of materials or equipment.

802.063 Conditional Uses:

802.0631  	Structures accessory to the uses listed in 802.061 above and the uses listed in 802.0632 – 	802.0638 below.

802.0632  	Extraction and storage of sand, gravel, and other materials.

802.0633  	Marinas, boat rentals, docks, piers, wharves, and water control structures.

802.0634  	Railroads, streets, bridges, utility transmission lines, and pipelines.

802.0635  	Storage yards for equipment, machinery, or materials.

802.0636 	Placement of fill or construction of fences.

802.0637  	Recreational vehicles either on individual lots of record or in existing or new subdivisions or 	commercial or condominium type campgrounds, subject to the exemptions and provisions of 	Section 802.113 of this Ordinance.

802.0638  	Structural works for flood control such as levees, dikes and floodwalls constructed to any 	height where the intent is to protect individual structures and levees or dikes where the intent 	is to protect agricultural crops for a frequency flood event equal to or less than the 10-year 	frequency flood event.

802.064 Standards for Floodway Conditional Uses:

802.0641  	All Uses.  No structure (temporary or permanent), fill (including fill for roads and levees), 	deposit, obstruction, storage of materials or equipment, or other uses may be allowed as a 	conditional use that will cause any increase in the stage of the 100-year or regional flood or 	cause an increase in flood damages in the reach or reaches affected.

802.0642  	All floodway conditional uses shall be subject to the procedures and standards contained in 	Section 802.124 of this Ordinance.

802.0643  	The conditional use shall be permissible in the underlying zoning district if one exists.

802.0644  	Fill:

(a) 	 	Fill, dredge spoil, and all other similar materials deposited or stored in the flood plain shall 	be protected from erosion by vegetative cover, mulching, riprap or other acceptable method.

(b) 		Dredge spoil sites and sand and gravel operations shall not be allowed in the floodway 	unless a long-term site development plan is submitted which includes an 	erosion/sedimentation prevention element to the plan.

(c) 	 	As an alternative, and consistent with Subsection (b) immediately above, dredge spoil 	disposal and sand and gravel operations may allow temporary, on-site storage of fill or other 	materials which would have caused an increase to the stage of the 100-year or regional flood 	but only after the Governing Body has received an appropriate plan which assures the 	removal of the materials from the floodway based upon the flood warning time available.  	The conditional use permit must be title registered with the property in the Office of the 	County Recorder.

802.0645  	Accessory Structures:

(a) 	 	Accessory structures shall not be designed for human habitation.

(b)  		Accessory structures, if permitted, shall be constructed and placed on the building site so as 	to offer the minimum obstruction to the flow of flood waters:

- Whenever possible, structures shall be constructed with the longitudinal axis parallel to the direction of flood flow; and

- So far as practicable, structures shall be placed approximately on the same flood flow lines as those of adjoining structures.

(c)  		Accessory structures shall be elevated on fill or structurally dry flood proofed in accordance 	with the FP-1 or FP-2 flood proofing classifications in the State Building Code.  As an 	alternative, an accessory structure may be flood proofed to the FP-3 or FP-4 flood proofing 	classification in the State Building Code provided the accessory structure constitutes a 	minimal investment, does not exceed 500 square feet in size at its largest projection, and for 	a detached garage, the detached garage must be used solely for parking of vehicles and 	limited storage.  All flood proofed accessory structures must meet the following additional 	standards:

- The structure must be adequately anchored to prevent flotation, collapse or lateral movement of the structure and shall be designed to equalize hydrostatic flood forces on exterior walls;

- Any mechanical and utility equipment in a structure must be elevated to or above the regulatory flood protection elevation or properly flood proofed; and

- To allow for the equalization of hydrostatic pressure, there must be a minimum of two

“automatic” openings in the outside walls of the structure having a total net area of not less than one square inch for every square foot of enclosed area subject to flooding.  There must be openings on at least two sides of the structure and the bottom of all openings must be no higher than one foot above the lowest adjacent grade to the structure.  Using human intervention to open a garage door prior to flooding will not satisfy this requirement for automatic openings.

802.0646  	Storage of Materials and Equipment:

(a)  		The storage or processing of materials that are, in time of flooding, flammable, explosive, or 	potentially injurious to human, animal, or plant life is prohibited.

(b)  		Storage of other materials or equipment may be allowed if readily removable from the area 	within the time available after a flood warning and in accordance with a plan approved by 	the Governing Body.

802.0647  	Structural works for flood control that will change the course, current or cross section of 	protected wetlands or public waters shall be subject to the provisions of Minnesota Statute, 	Chapter 103G.  Community-wide structural works for flood control intended to remove areas 	from the regulatory flood plain shall not be allowed in the floodway.

802.0648  	A levee, dike or floodwall constructed in the floodway shall not cause an increase to the 100-	year or regional flood and the technical analysis must assume equal conveyance or storage 	loss on both sides of a stream.

SECTION  802.07 FLOOD FRINGE DISTRICT (FF)

802.071 Permitted Uses:  Permitted uses shall be those uses of land or structures listed as permitted uses in the underlying zoning use district(s).  If no pre-existing, underlying zoning use districts exist, then any residential or non residential structure or use of a structure or land shall be a permitted use in the Flood Fringe District provided such use does not constitute a public nuisance.  All permitted uses shall comply with the standards for Flood Fringe District “Permitted Uses” listed in Section 802.072 and the "Standards for all Flood Fringe Uses" listed in Section 802.075.

802.072 Standards for Flood Fringe Permitted Uses:

802.0721  	All structures, including accessory structures, must be elevated on fill so that the lowest floor 	including basement floor is at or above the regulatory flood protection elevation.  The 		finished fill elevation for structures shall be no lower than one (1) foot below the regulatory 	flood protection elevation and the fill shall extend at such elevation at least fifteen (15) feet 	beyond the outside limits of the structure erected thereon.

802.0722  	As an alternative to elevation on fill, accessory structures that constitute a minimal 	investment and that do not exceed 500 square feet at its largest projection may be internally 	flood proofed in accordance with Section 802.0645 (c).

802.0723  	The cumulative placement of fill where at any one time in excess of one-thousand (1,000) 	cubic yards of fill is located on the parcel shall be allowable only as a conditional use, unless 	said fill is specifically intended to elevate a structure in accordance with Section 802.0721 of 	this ordinance.

802.0724  	The storage of any materials or equipment shall be elevated on fill to the regulatory flood 	protection elevation.

802.0725  	The provisions of Section 802.075 of this Ordinance shall apply.

802.073 Conditional Uses:  Any structure that is not elevated on fill or flood proofed in accordance with Section 802.0721 – 802.0722 and or any use of land that does not comply with the standards in Section 802.0723 – 802.0724 shall only be allowable as a conditional use.  An application for a conditional use shall be subject to the standards and criteria and evaluation procedures specified in Sections 802.074-807.075 and 802.124 of this Ordinance.

802.074 Standards for Flood Fringe Conditional Uses:

802.0741  	Alternative elevation methods other than the use of fill may be utilized to elevate a 	structure's lowest floor above the regulatory flood protection elevation.  These alternative 	methods may include the use of stilts, pilings, parallel walls, etc., or above-grade, enclosed 	areas such as crawl spaces or tuck under garages.  The base or floor of an enclosed area shall 	be considered above-grade and not a structure's basement or lowest floor if:  1) the enclosed 	area is above-grade on at least one side of the structure; 2) it is designed to internally flood 	and is constructed with flood resistant materials; and 3) it is used solely for parking of 	vehicles, building access or storage.  The above-noted alternative elevation methods are 	subject to the following additional standards:

(a)  		Design and Certification - The structure's design and as-built condition must be certified by a 	registered professional engineer or architect as being in compliance with the general design 	standards of the State Building Code and, specifically, that all electrical, heating, ventilation, 	plumbing and air conditioning equipment and other service facilities must be at or above the 	regulatory flood protection elevation or be designed to prevent flood water from entering or 	accumulating within these components during times of flooding.

(b) 	 	Specific Standards for Above-grade, Enclosed Areas - Above-grade, fully enclosed areas 	such as crawl spaces or tuck under garages must be designed to internally flood and the 	design plans must stipulate:

- A minimum area of openings in the walls where internal flooding is to be used as a flood proofing technique.  There shall be a minimum of two openings on at least two sides of the structure and the bottom of all openings shall be no higher than one-foot above grade.  The automatic openings shall have a minimum net area of not less than one square inch for every square foot of enclosed area subject to flooding unless a registered professional engineer or architect certifies that a smaller net area would suffice.  The automatic openings may be equipped with screens, louvers, valves, or other coverings or devices provided that they permit the automatic entry and exit of flood waters without any form of human intervention; and

- That the enclosed area will be designed of flood resistant materials in accordance with the FP-3 or FP-4 classifications in the State Building Code and shall be used solely for building access, parking of vehicles or storage.

802.0742  	Basements, as defined by Section 802.0482 of this Ordinance, shall be subject to the 	following:

(a) 	 	Residential basement construction shall not be allowed below the regulatory flood protection 	elevation.

(b) 	 	Non-residential basements may be allowed below the regulatory flood protection elevation 	provided the basement is structurally dry flood proofed in accordance with Section 802.0743 	of this Ordinance.

802.0743  	All areas of non residential structures including basements to be placed below the regulatory 	flood protection elevation shall be flood proofed in accordance with the structurally dry 	flood proofing classifications in the State Building Code.  Structurally dry flood proofing 	must meet the FP-1 or FP-2 flood proofing classification in the State Building Code and this 	shall require making the structure watertight with the walls substantially impermeable to the 	passage of water and with structural components having the capability of resisting 	hydrostatic and hydrodynamic loads and the effects of buoyancy.  Structures flood proofed 	to the FP-3 or FP-4 classification shall not be permitted.

802.0744  	Storage of Materials and Equipment:

(a)  		The storage or processing of materials that are, in time of flooding, flammable, explosive, or 	potentially injurious to human, animal, or plant life is prohibited.

(b)  		Storage of other materials or equipment may be allowed if readily removable from the area 	within the time available after a flood warning and in accordance with a plan approved by 	the Governing Body.

802.0745  	The provisions of Section 802.075 of this Ordinance shall also apply.

802.075 Standards for All Flood Fringe Uses:

802.0751	This Section Reserved For Future Use.

802.0752  	Commercial Uses - accessory land uses, such as yards, railroad tracks, and parking lots may 	be at elevations lower than the regulatory flood protection elevation.  However, a permit for 	such facilities to be used by the employees or the general public shall not be granted in the 	absence of a flood warning system that provides adequate time for evacuation if the area 	would be inundated to a depth and velocity such that when multiplying the depth (in feet) 	times velocity (in feet per second) the product number exceeds four (4) upon occurrence of 	the regional flood.

802.0753  	Manufacturing and Industrial Uses - measures shall be taken to minimize interference with 	normal plant operations especially along streams having protracted flood durations.  Certain 	accessory land uses such as yards and parking lots may be at lower elevations subject to 	requirements set out in Section 802.0752 above.  In considering permit applications, due 	consideration shall be given to needs of an industry whose business requires that it be 	located in flood plain areas.

802.0754  	Fill shall be properly compacted and the slopes shall be properly protected by the use of 	riprap, vegetative cover or other acceptable method.  The Federal Emergency Management 	Agency (FEMA) has established criteria for removing the special flood hazard area 	designation for certain structures properly elevated on fill above the 100-year flood elevation 	- FEMA's requirements incorporate specific fill compaction and side slope protection 	standards for multi-structure or multi-lot developments.  These standards should be 	investigated prior to the initiation of site preparation if a change of special flood hazard area 	designation will be requested.

802.0755  	Flood plain developments shall not adversely affect the hydraulic capacity of the channel 	and adjoining flood plain of any tributary watercourse or drainage system where a floodway 	or other encroachment limit has not been specified on the Official Zoning Map.

802.0756  	Standards for recreational vehicles are contained in Section 802.113.

802.0757  	All manufactured homes must be securely anchored to an adequately anchored foundation 	system that resists flotation, collapse and lateral movement.  Methods of anchoring may 	include, but are not to be limited to, use of over-the-top or frame ties to ground anchors.  	This requirement is in addition to applicable state or local anchoring requirements for 	resisting wind forces.

# SECTION 802.08 RESERVED FOR FUTURE USE

SECTION  802.09 SUBDIVISIONS2

802.091 Review Criteria:  No land shall be subdivided which is unsuitable for the reason of flooding, inadequate drainage, water supply or sewage treatment facilities.  All lots within the flood plain districts shall be able to contain a building site outside of the Floodway District at or above the regulatory flood protection elevation.  All subdivisions shall have water and sewage treatment facilities that comply with the provisions of this Ordinance and have road access both to the subdivision and to the individual building sites no lower than two feet below the regulatory flood protection elevation.  For all subdivisions in the flood plain, the Floodway and Flood Fringe District boundaries, the regulatory flood protection elevation and the required elevation of all access roads shall be clearly labeled on all required subdivision drawings and platting documents.

802.092 Removal of Special Flood Hazard Area Designation:  The Federal Emergency Management Agency (FEMA) has established criteria for removing the special flood hazard area designation for certain structures properly elevated on fill above the 100-year flood elevation.  FEMA's requirements incorporate specific fill compaction and side slope protection standards for multi-structure or multi-lot developments.  These standards should be investigated prior to the initiation of site preparation if a change of special flood hazard area designation will be requested.

# SECTION  802.10 PUBLIC UTILITIES, RAILROADS, ROADS, AND BRIDGES

802.101 Public Utilities.  All public utilities and facilities such as gas, electrical, sewer, and water supply systems to be located in the flood plain shall be flood proofed in accordance with the State Building Code or elevated to above the regulatory flood protection elevation.

802.102 Public Transportation Facilities.  Railroad tracks, roads, and bridges to be located within the flood plain shall comply with Sections 802.06 and 802.07 of this Ordinance.  Elevation to the regulatory flood protection elevation shall be provided where failure or interruption of these transportation facilities would result in danger to the public health or safety or where such facilities are essential to the orderly functioning of the area.  Minor or auxiliary roads or railroads may be constructed at a lower elevation where failure or interruption of transportation services would not endanger the public health or safety.

802.103 On-site Sewage Treatment and Water Supply Systems:  Where public utilities are not provided:  1) On-site water supply systems must be designed to minimize or eliminate infiltration of flood waters into the systems; and 2) New or replacement on-site sewage treatment systems must be designed to minimize or eliminate infiltration of flood waters into the systems and discharges from the systems into flood waters and they shall not be subject to impairment or contamination during times of flooding.  Any sewage treatment system designed in accordance with the State's current statewide standards for on-site sewage treatment systems shall be determined to be in compliance with this Section.

SECTION  802.11 MANUFACTURED HOMES AND MANUFACTURED HOME PARKS AND PLACEMENT OF RECREATIONAL VEHICLES.

802.111 New manufactured home parks and expansions to existing manufactured home parks shall be subject to the provisions placed on subdivisions by Section 802.09 of this Ordinance.

802.112 The placement of new or replacement manufactured homes in existing manufactured home parks or on individual lots of record that are located in flood plain districts will be treated as a new structure and may be placed only if elevated in compliance with Section 802.07 of this Ordinance.

802.1121  	All manufactured homes must be securely anchored to an adequately anchored foundation 	system that resists flotation, collapse and lateral movement.  Methods of anchoring may 	include, but are not to be limited to, use of over-the-top or frame ties to ground anchors.  	This requirement is in addition to applicable state or local anchoring requirements for 	resisting wind forces.

802.113 Recreational vehicles that do not meet the exemption criteria specified in Section 802.1131 below shall be subject to the provisions of this Ordinance and as specifically spelled out in Sections 802.1133-802.1134 below.

802.1131  	Exemption - Recreational vehicles are exempt from the provisions of this Ordinance if they 	are placed in any of the areas listed in Section 802.1132 below and further they meet the 	following criteria:

(a) 	 	Have current licenses required for highway use.

(b)  		Are highway ready meaning on wheels or the internal jacking system, are attached to the site 	only by quick disconnect type utilities commonly used in campgrounds and recreational 	vehicle parks and the recreational vehicle has no permanent structural type additions 	attached to it.

(c) 	 	The recreational vehicle and associated use must be permissible in any pre-existing, 	underlying zoning use district.

802.1132  	Areas Exempted For Placement of Recreational Vehicles:

(a)  		Individual lots or parcels of record.

(b) 	 	Existing commercial recreational vehicle parks or campgrounds.

(c)  		Existing condominium type associations.

802.1133	Recreational vehicles exempted in Section 802.1131 lose this exemption when 				development occurs on the parcel exceeding $500 for a structural addition to the recreational 		vehicle or exceeding $500 for an accessory structure such as a garage or storage building.  		The recreational vehicle and all additions and accessory structures will then be treated as a 		new structure and shall be subject to the elevation/flood proofing requirements and the use 		of land restrictions specified in Sections 802.06 and 802.07 of this Ordinance.  There shall 		be no development or improvement on the parcel or attachment to the recreational vehicle 		that hinders the removal of the recreational vehicle to a flood free location should flooding 		occur.

802.114  	New commercial recreational vehicle parks or campgrounds and new residential type 	subdivisions and condominium associations and the expansion of any existing similar use 	exceeding five (5) units or dwelling sites shall be subject to the following:

(a)  Any new or replacement recreational vehicle will be allowed in the Flood Fringe                 	Districts provided said recreational vehicle and its contents are placed on fill above the 	regulatory flood protection elevation.

(b)  All new or replacement recreational vehicles not meeting the criteria of (a) above may, 	as an alternative, be allowed as a conditional use if in accordance with the following 	provisions and the provisions of 802.124 of the Ordinance.  The applicant must submit an 	emergency plan for the safe evacuation of all vehicles and people during the 100 year flood.  	Said plan shall be prepared by a registered engineer or other qualified individual, shall 	demonstrate that adequate time and personnel exist to carry out the evacuation, and shall 	demonstrate the provisions of Section 802.1131 (a) and (b) of this Ordinance will be met. All 	attendant sewage and water facilities for new or replacement recreational vehicles must be 	protected or constructed so as to not be impaired or contaminated during times of flooding in 	accordance with Section 802.103 of this Ordinance.

# SECTION  802.12   ADMINISTRATION

802.121 Zoning Administrator:  A Zoning Administrator or other official designated by the Governing Body shall administer and enforce this Ordinance.  If the Zoning Administrator finds a violation of the provisions of this Ordinance the Zoning Administrator shall notify the person responsible for such violation in accordance with the procedures stated in Section 802.14 of the Ordinance.

802.122  Permit Requirements:

802.1221 Permit Required.  A Permit issued by the Zoning Administrator in conformity with the 	provisions of this Ordinance shall be secured prior to the erection, addition, modification, 	rehabilitation (including normal maintenance and repair), or alteration of any building, 	structure, or portion thereof; prior to the use or change of use of a building, structure, or 	land; prior to the construction of a dam, fence, or on-site septic system; prior to the change 	or extension of a nonconforming use; prior to the repair of a structure that has been damaged 	by flood, fire, tornado, or any other source; and prior to the placement of fill, excavation of 	materials, or the storage of materials or equipment within the flood plain.

802.1222 	Application for Permit.  Application for a permit shall be made in duplicate to the Zoning 	Administrator on forms furnished by the Zoning Administrator and shall include the 	following where applicable:  plans in duplicate drawn to scale, showing the nature, location, 	dimensions, and elevations of the lot; existing or proposed structures, fill, or storage of 	materials; and the location of the foregoing in relation to the stream channel.

802.1223 	State and Federal Permits.  Prior to granting a permit or processing an application for a 	conditional use permit or variance, the Zoning Administrator shall determine that the 	applicant has obtained all necessary state and federal permits.

802.1224 Certificate of Zoning Compliance for a New, Altered, or Nonconforming Use.  It shall be 	unlawful to use, occupy, or permit the use or occupancy of any building or premises or part 	thereof hereafter created, erected, changed, converted, altered, or enlarged in its use or 	structure until a certificate of zoning compliance shall have been issued by the Zoning 	Administrator stating that the use of the building or land conforms to the requirements of this 	Ordinance.

802.1225	Construction and Use to be as Provided on Applications, Plans, Permits, Variances and 	Certificates of Zoning Compliance.  Permits, conditional use permits, or certificates of 	zoning compliance issued on the basis of approved plans and applications authorize only the 	use, arrangement, and construction set forth in such approved plans and applications, and no 	other use, arrangement, or construction.  Any use, arrangement, or construction at variance 	with that authorized shall be deemed a violation of this Ordinance, and punishable as 	provided by Section 802.14 of this Ordinance.

802.1226 	Certification.  The applicant shall be required to submit certification by a registered 	professional engineer, registered architect, or registered land surveyor that the finished fill 	and building elevations were accomplished in compliance with the provisions of this 	Ordinance.  Flood proofing measures shall be certified by a registered professional engineer 	or registered architect.

802.1227 	Record of First Floor Elevation.  The Zoning Administrator shall maintain a record of the 	elevation of the lowest floor (including basement) of all new structures and alterations or 	additions to existing structures in the flood plain.  The Zoning Administrator shall also 	maintain a record of the elevation to which structures or alterations and additions to 	structures are flood proofed.

802.1228 	Notifications for Watercourse Alterations.  The Zoning Administrator shall notify, in 	riverine situations, adjacent communities and the Commissioner of the Department of 	Natural Resources prior to the community authorizing any alteration or relocation of a 	watercourse.  If the applicant has applied for a permit to work in the beds of public waters 	pursuant to Minnesota Statute, Chapter 103G, this shall suffice as adequate notice to the 	Commissioner of Natural Resources.  A copy of said notification shall also be submitted to 	the Chicago Regional Office of the Federal Emergency Management Agency (FEMA).

802.1229 	Notification to FEMA When Physical Changes Increase or Decrease the 100-year Flood 	Elevation.  As soon as is practicable, but not later than six (6) months after the date such 	supporting information becomes available, the Zoning Administrator shall notify the 	Chicago Regional Office of FEMA of the changes by submitting a copy of said technical or 	scientific data.

802.123   Board of Adjustment:

802.1231 	Rules.  The Board of Adjustment shall adopt rules for the conduct of business and may 	exercise all of the powers conferred on such Boards by State law.

802.1232 	Administrative Review.  The Board of Adjustment shall hear and decide appeals where it is 	alleged there is error in any order, requirement, decision, or determination made by an 	administrative official in the enforcement or administration of this Ordinance.

802.1233 	Variances.  The Board of Adjustment may authorize upon appeal in specific cases such relief 	or variance from the terms of this Ordinance as will not be contrary to the public interest and 	only for those circumstances such as hardship, practical difficulties or circumstances unique 	to the property under consideration, as provided for in the respective enabling legislation for 	planning and zoning for cities or counties as appropriate.  In the granting of such variance, 	the Board of Adjustment shall clearly identify in writing the specific conditions that existed 	consistent with the criteria specified in this Ordinance, any other zoning regulations in the 	Community, and in the respective enabling legislation that justified the granting of the 	variance.  No variance shall have the effect of allowing in any district uses prohibited in that 	district, permit a lower degree of flood protection than the regulatory flood protection 	elevation for the particular area, or permit standards lower than those required by state law.  	The following additional variance criteria of the Federal Emergency Management Agency 	must be satisfied:

(a) 	 Variances shall not be issued by a community within any designated regulatory floodway if 	any increase in flood levels during the base flood discharge would result.

(b) 	 	Variances shall only be issued by a community upon (i) a showing of good and sufficient 	cause, (ii) a determination that failure to grant the variance would result in exceptional 	hardship to the applicant, and (iii) a determination that the granting of a variance will not 	result in increased flood heights, additional threats to public safety, extraordinary public 	expense, create nuisances, cause fraud on or victimization of the public, or conflict with 	existing local laws or ordinances.

(c) 	 Variances shall only be issued upon a determination that the variance is the minimum 	necessary, considering the flood hazard, to afford relief.

802.1234 	Hearings.  Upon filing with the Board of Adjustment of an appeal from a decision of the 	Zoning Administrator, or an application for a variance, the Board of Adjustment shall fix a 	reasonable time for a hearing and give due notice to the parties in interest as specified by 	law.  The Board of Adjustment shall submit by mail to the Commissioner of Natural 	Resources a copy of the application for proposed variances sufficiently in advance so that 	the Commissioner will receive at least ten days notice of the hearing.

802.1235 	Decisions.  The Board of Adjustment shall arrive at a decision on such appeal or variance 	within 30 days.  In passing upon an appeal, the Board of Adjustment may, so long as such 	action is in conformity with the provisions of this Ordinance, reverse or affirm, wholly or in 	part, or modify the order, requirement, decision or determination of the Zoning 	Administrator or other public official.  It shall make its decision in writing setting forth the 	findings of fact and the reasons for its decisions.  In granting a variance the Board of 	Adjustment may prescribe appropriate conditions and safeguards such as those specified in 	Section 802.1246, which are in conformity with the purposes of this Ordinance.  Violations 	of such conditions and safeguards, when made a part of the terms under which the variance 	is granted, shall be deemed a violation of this Ordinance punishable under Section 802.14.  	A copy of all decisions granting variances shall be forwarded by mail to the Commissioner 	of Natural Resources within ten (10) days of such action.

802.1236 	Appeals.  Appeals from any decision of the Board of Adjustment may be made, and as 	specified in this community's official controls and also by Minnesota Statutes.

802.1237 	Flood Insurance Notice and Record Keeping.  The Zoning Administrator shall notify the 	applicant for a variance that:  1) The issuance of a variance to construct a structure below the 	base flood level will result in increased premium rates for flood insurance up to amounts as 	high as $25 for $100 of insurance coverage and 2) Such construction below the 100-year or 	regional flood level increases risks to life and property.  Such notification shall be 	maintained with a record of all variance actions.  A community shall maintain a record of all 	variance actions, including justification for their issuance, and report such variances issued 	in its annual or biennial report submitted to the Administrator of the National Flood 	Insurance Program.

802.124  Conditional Uses.  The Mendota City Council shall hear and decide applications for conditional uses permissible under this Ordinance.  Applications shall be submitted to the Zoning Administrator who shall forward the application to The Mendota City Council for consideration.

802.1241 	Hearings.  Upon filing with the Mendota City Council an application for a conditional use 	permit, the Mendota City Council shall submit by mail to the Commissioner of Natural 	Resources a copy of the application for proposed conditional use sufficiently in advance so 	that the Commissioner will receive at least ten days notice of the hearing.

802.1242 	Decisions.  The Mendota City Council shall arrive at a decision on a conditional use 	within 30 days.  In granting a conditional use permit the Mendota City Council shall 	prescribe appropriate conditions and safeguards, in addition to those specified in Section 	802.1246, which are in conformity with the purposes of this Ordinance.  Violations of such 	conditions and safeguards, when made a part of the terms under which the conditional use 	permit is granted, shall be deemed a violation of this Ordinance punishable under Section 	802.14.  A copy of all decisions granting conditional use permits shall be forwarded by mail 	to the Commissioner of Natural Resources within ten (10) days of such action.

802.1243	Procedures to be followed by the Mendota City Council in Passing on Conditional Use 	Permit Applications Within all Flood Plain Districts.

(a)  		Require the applicant to furnish such of the following information and additional 	information as deemed necessary by the Mendota City Council for determining the 	suitability of the particular site for the proposed use:

- Plans in triplicate drawn to scale showing the nature, location, dimensions, and elevation of the lot, existing or proposed structures, fill, storage of materials, flood proofing measures, and the relationship of the above to the location of the stream channel; and

- Specifications for building construction and materials, flood proofing, filling, dredging, grading, channel improvement, storage of materials, water supply and sanitary facilities.

(b)  		Transmit one copy of the information described in subsection (a) to a designated engineer or 	other expert person or agency for technical assistance, where necessary, in evaluating the 	proposed project in relation to flood heights and velocities, the seriousness of flood damage 	to the use, the adequacy of the plans for protection, and other technical matters.

(c)  		Based upon the technical evaluation of the designated engineer or expert, the Mendota City 	Council shall determine the specific flood hazard at the site and evaluate the suitability of the 	proposed use in relation to the flood hazard.

802.1244 	Factors Upon Which the Decision of the Mendota City Council Shall Be Based.  In 	passing upon conditional use applications, the Mendota City Council shall consider all 	relevant factors specified in other sections of this Ordinance, and:

(a)  		The danger to life and property due to increased flood heights or velocities caused by 	encroachments.

(b)  		The danger that materials may be swept onto other lands or downstream to the injury of 	others or they may block bridges, culverts or other hydraulic structures.

(c) 	 	The proposed water supply and sanitation systems and the ability of these systems to prevent 	disease, contamination, and unsanitary conditions.

(d)  		The susceptibility of the proposed facility and its contents to flood damage and the effect of 	such damage on the individual owner.

(e)  		The importance of the services provided by the proposed facility to the community.

(f)  		The requirements of the facility for a waterfront location.

(g)  		The availability of alternative locations not subject to flooding for the proposed use.

(h) 	 	The compatibility of the proposed use with existing development and development 	anticipated in the foreseeable future.

(i)  		The relationship of the proposed use to the comprehensive plan and flood plain management 	program for the area.

(j)  		The safety of access to the property in times of flood for ordinary and emergency vehicles.

(k)  		The expected heights, velocity, duration, rate of rise, and sediment transport of the flood 	waters expected at the site.

(l)  		Such other factors which are relevant to the purposes of this Ordinance.

802.1245 	Time for Acting on Application.  The Mendota City Council shall act on an application in 	the manner described above within 30 days from receiving the application, except 	that where additional information is required pursuant to 802.1243 of this Ordinance.  The 	Mendota City Council shall render a written decision within 30 days from the receipt of such 	additional information.

802.1246 	Conditions Attached to Conditional Use Permits.  Upon consideration of the factors listed 	above and the purpose of this Ordinance, the Mendota City Council shall attach such 	conditions to the granting of conditional use permits as it deems necessary to fulfill the 	purposes of this Ordinance.  Such conditions may include, but are not limited to, the 	following:

(a)  		Modification of waste treatment and water supply facilities.

(b)  		Limitations on period of use, occupancy, and operation.

(c) 	 	Imposition of operational controls, sureties, and deed restrictions.

(d) 	 	Requirements for construction of channel modifications, compensatory storage, dikes, 	levees, and other protective measures.

(e) 	 	Flood proofing measures, in accordance with the State Building Code and this Ordinance.  	The applicant shall submit a plan or document certified by a registered professional engineer 	or architect that the flood proofing measures are consistent with the regulatory flood 	protection elevation and associated flood factors for the particular area.

# SECTION  802.13   NONCONFORMING USES

802.131 A structure or the use of a structure or premises which was lawful before the passage or amendment of this Ordinance but which is not in conformity with the provisions of this Ordinance may be continued subject to the following conditions.  Historic structures, as defined in Section 802.04821(b) of this Ordinance, shall be subject to the provisions of Sections 802.1311 – 802.1315 of this Ordinance.

802.1311	 No such use shall be expanded, changed, enlarged, or altered in a way that increases its 	nonconformity.

802.1312 	Any structural alteration or addition to a nonconforming structure or nonconforming use 	which would result in increasing the flood damage potential of that structure or use shall be 	protected to the Regulatory Flood Protection Elevation in accordance with any of the 	elevation on fill or flood proofing techniques (i.e., FP-1 thru FP-4 floodproofing 	classifications) allowable in the State Building Code, except as further restricted in 802.1313 	and 802.1316 below.

802.1313 	The cost of all structural alterations or additions to any nonconforming structure over the life 	of the structure shall not exceed 50 percent of the market value of the structure unless the 	conditions of this Section are satisfied.  The cost of all structural alterations and additions 	must include all costs such as construction materials and a reasonable cost placed on all 	manpower or labor.  If the cost of all previous and proposed alterations and additions 	exceeds 50 percent of the market value of the structure, then the structure must meet the 	standards of Section 802.06 or 802.07 of this Ordinance for new structures depending upon 	whether the structure is in the Floodway or Flood Fringe District, respectively.

802.13l4	If any nonconforming use is discontinued for l2 consecutive months, any future use of the 	building premises shall conform to this Ordinance.  The Assessor shall notify the Zoning 	Administrator in writing of instances of nonconforming uses that have been discontinued for 	a period of l2 months.

802.1315	If any nonconforming use or structure is substantially damaged, as defined in Section 			802.04820 of this Ordinance, it shall not be reconstructed except in conformity with the 			provisions of this Ordinance.  The applicable provisions for establishing new uses or new 		structures in Sections 802.06 and 802.07 will apply depending upon whether the use or 			structure is in the Floodway or Flood Fringe District, respectively.

802.1316 	If a substantial improvement occurs, as defined in Section 802.04821 of this Ordinance, 	from any combination of a building addition to the outside dimensions of the existing 	building or a rehabilitation, reconstruction, alteration, or other improvement to the inside 	dimensions of an existing nonconforming building, then the building addition and the 	existing nonconforming building must meet the requirements of Section 802.06 or 802.07 of 	this Ordinance for new structures, depending upon whether the structure is in the Floodway 	or Flood Fringe District, respectively.

## SECTION 802.14 PENALTIES FOR VIOLATION

802.141   Violation of the provisions of this Ordinance or failure to comply with any of its requirements (including violations of conditions and safeguards established in connection with grants of variances or conditional uses) shall constitute a misdemeanor and shall be punishable as defined by law.

802.142   Nothing herein contained shall prevent the City of Mendota from taking such other lawful action as is necessary to prevent or remedy any violation.  Such actions may include but are not limited to:

802.1421 	In responding to a suspected Ordinance violation, the Zoning Administrator and Local 	Government may utilize the full array of enforcement actions available to it including but 	not limited to prosecution and fines, injunctions, after-the-fact permits, orders for corrective 	measures or a request to the National Flood Insurance Program for denial of flood insurance 	availability to the guilty party.  The Community must act in good faith to enforce these 	official controls and to correct Ordinance violations to the extent possible so as not to 	jeopardize its eligibility in the National Flood Insurance Program.

802.1422 	When an Ordinance violation is either discovered by or brought to the attention of the 	Zoning Administrator, the Zoning Administrator shall immediately investigate the situation 	and document the nature and extent of the violation of the official control.  As soon as is 	reasonably possible, this information will be submitted to the appropriate Department of 	Natural Resources' and Federal Emergency Management Agency Regional Office along with 	the Community's plan of action to correct the violation to the degree possible.

802.1423 	The Zoning Administrator shall notify the suspected party of the requirements of this 	Ordinance and all other official controls and the nature and extent of the suspected violation 	of these controls.  If the structure and/or use are under construction or development, the 	Zoning Administrator may order the construction or development immediately halted until a 	proper permit or approval is granted by the Community.  If the construction or development 	is already completed, then the Zoning Administrator may either: (1) issue an order 	identifying the corrective actions that must be made within a specified time period to bring 	the use or structure into compliance with the official controls; or (2) notify the responsible 	party to apply for an after-the-fact permit/development approval within a specified period of 	time not to exceed 30-days.

802.1424 	If the responsible party does not appropriately respond to the Zoning Administrator within 	the specified period of time, each additional day that lapses shall constitute an additional 	violation of this Ordinance and shall be prosecuted accordingly.  The Zoning Administrator 	shall also upon the lapse of the specified response period notify the landowner to restore the 	land to the condition which existed prior to the violation of this Ordinance.

# SECTION 802.15 AMENDMENTS

The flood plain designation on the Official Zoning Map shall not be removed from flood plain areas unless it can be shown that the designation is in error or that the area has been filled to or above the elevation of the regulatory flood protection elevation and is contiguous to lands outside the flood plain.  Special exceptions to this rule may be permitted by the Commissioner of Natural Resources if he determines that, through other measures, lands are adequately protected for the intended use.

All amendments to this Ordinance, including amendments to the Official Zoning Map, must be submitted to and approved by the Commissioner of Natural Resources prior to adoption.  Changes in the Official Zoning Map must meet the Federal Emergency Management Agency's (FEMA) Technical Conditions and Criteria and must receive prior FEMA approval before adoption.  The Commissioner of Natural Resources must be given 10-days written notice of all hearings to consider an amendment to this Ordinance and said notice shall include a draft of the Ordinance amendment or technical study under consideration.

EFFECTIVE DATE:  This Ordinance shall be in full force and effect from and after its passage and approval and publication, as required by law and/or charter.

Adopted by the _City of Mendota City Council

This _9_ of _August_, _2011_

Attest:  ______________________  ___, Mayor

Brian Mielke

Attest:  __________________________, City Clerk

Jennifer Bruestle

Stamp With Community Seal: